## Slide 1: Karabo Integrating Control, Data Acquisition, Data Management, and Data Analysis Tasks into a Single Software Framework
Burkhard Heisen
Control and Analysis Software Group – European XFEL GmbH
European XFEL User’s Meeting
Hamburg, January 28, 2015
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Karabo will be used at the photon beamlines
Karabo
DOOCS Tine EPICS
Why?
  One software framework, one user interface, one programming interface
  Less learning, less teaching, less maintenance, less changes, less conversions, more freedom
Why else?
  Our requirements are different to those of classical synchrotron or high energy physics experiments
  We invest a lot of money for better science, a small fraction is for better software

## Slide 3: The vision – From a user perspective
DAQ
data readout
online processing
quality monitoring (vetoing)
DA
processing pipelines
distributed and GPU computing
specific algorithms (e.g. reconstruction)
Control
drive hardware and complex experiments
monitor variables & trigger alarms
DM
storage of experiment & control data
data access, authentication authorization etc.
setup computation & show scientific results
allow some control & show hardware status
show online data whilst running
A typical use case:
Accelerator
Undulator
Beam Transport
Sample Injector
DM
DA
Control
DAQ
Tight integration of applications
Notes: In order to understand what software we need image a prospective user wanting to conduct an experiment at XFEL in 2015!
300 images per train = 1.000.000 images after 5 min 30 s
512 image per train = 1.000.000 images after 3 min 15 s
~ 4 TB dataset
Tuning means:
Visualize whether any sample get hit. Re-configure injector.
Start, stop acquisition etc…
Starting experiment means:
Get detector, injector etc. ready to go (control)
Prepare storage system for sinking data with 10 GB/s

## Slide 4: The vision – From a data perspective
Courtesy of S. Hauf

## Slide 5: Karabo is a “device” based system
Equipment
Control
e.g. motor, pump, valve, sensor
DAQ
Equipment
e.g. commercial camera
Service
Device
e.g. calibrationManager, configurationManager
Analysis
Node
e.g. calibrationManager, projectManager, GUI server
Data Storage
Node
e.g. storage of data from runs
e.g. 2D-detectors (AGIPD, LPD, DSSC)
DAQ
Equipment
Composite
Device
e.g. complex detector motion control
DM
DA
Control
DAQ
Message Broker
User interface(s)

## Slide 6: Device – As controllable object
  Device classes can be loaded at runtime (plugin technology)
  Can be written in C++ or Python
  Devices completely describe themselves. Allows automatic GUI creation
  Runtime-extension of properties, commands and attributes is possible
  Hierarchical groupings of parameters are possible
  Any property setting or command execution can be restricted to a set of allowed states
  The GUI reflects state limitations by enabling/disabling buttons and properties dynamically
Attribute
Property
Command
auto generated

## Slide 7: Device – As pipeline module
Devices can act as modules of a streaming data pipeline
  Configurable generic input/output channels on devices
  Developers just need to code the onData and (optionally) the onEndOfStream method
  IO system is decoupled from processing system (process whilst transferring data)
  Input channels configure whether they share the sent data amongst all input channels or whether they receive a copy of each data token
  Broker-based communication transparently establishes a point-to-point connection
  Any pipeline device has full access to the live control-system (feedbacks easily possible)
TCP
Memory
Multi-threaded processing
Distributed processing

## Slide 8: Pipelines support load balancing
IO whilst computing
Pixel parallel processing
(one GPU thread per pixel)
Notification about new data possible to obtain
GPU
CPU
Once resources are available, input channels request new data from connected output channels
Configurable output channel behavior in case no input currently available: error, queue, wait, drop

## Slide 9: Graphical interface - Overview
drag & drop
Live Navigation
Custom Scene
Configuration
Project
Log Messages
Interactive Command Line
Documentation
Bug Reporting
User centric and access-controlled setup (login at startup)
Dock-able and resizable multi-panel, all-in-one user interface
Live navigation showing all device-servers, plugins, and device instances
Automatically generated configuration panel, allowing to read/write/execute
Project panel for persisting configurations, macros, scenes, resources, etc.
PowerPoint like, drag & droppable, tabbed custom scene
Centralized logging information, notification handling, documentation, etc.

## Slide 10: Graphical interface – Pipelines and Macros
drag & drop
Courtesy of K. Weger
Courtesy of M. Teichmann
Pipeline configuration
  Whole devices can be dragged (from left side) as pipeline nodes
  Dragging individual parameters from right is still possible (e.g. control parameters)
  Devices can be grouped and edited as group (connections and configurations)
Macro editing
  Editing and execution from within GUI or using regular terminal
  Macro parameters and functions integrate automatically into configuration panel
  Macro API can be interactively executed in embedded IPython interpreter
  Macro writing is something we hope our users can easily do themselves

## Slide 11: Cameras, power supplies, heaters…
Supported standards
  GenICam (generic interface for cameras) - industry standard
  Lima (library for image acquisition) – ESRF project
  SPCI (Standard Commands for Programmable Instruments)
Cameras
  Basler (all GigE), Photonic Science (sCMOS)
  IMPERX (Bobcat B4020), Andor (Neo)
  AVT (all Prosilica), Axis (all)
Other devices
  FUG, Heinziger (power supplies), TEM (beam lock)
  Amphos (laser power stage)
  EnergyMax (laser sensors)
  Lakeshore (heater), STS (spectrometer)

## Slide 12: Motors, pumps, valves… and real-time control
Karabo itself does not directly provide real-time processes/communications -> uses Beckhoff layer
Beckhoff PLC-firmware blocks are mapped to Karabo devices and can be auto-generated from PLC self-description
Integrated devices (now extending to different vendors):
  Turbo-, ion-, and scroll-pumps
  Valves, gauges, temperature sensors
  Stepper-, piezo- and servo-motors
Beck
Com
Motor1
Motor2
Pump1
PLC-CPU
Motor1
Motor2
Pump1
TCP (own protocol)
Gather/Scatter
EtherCAT
Courtesy of P. Geßler

## Slide 13: Digitizers, ADCs, Timing interfaces…
Digitizers (used in XGMs, PESs)
Fast ADCs (analog to digital converters)
Timing interfaces (in progress)
Simulink/Matlab based FPGA programming framework with Karabo integration
SIS8300 – ADC AMC
(Struck Innovative Systems)
Final Design
Software
(Karabo)
XML FILE
  User Registers and Memories Description
  with script
Source Files
  Bus protocol logic generated automatically
MicroTCA crate
ADQ 412 (SP-Devices)
FPGA compiler/tool
Courtesy of P. Geßler

## Slide 14: Karabo in use – Control systems
Pump probe laser setup (laser group)
  Runs burst mode according to XFEL (4.5 MHz intra burst)
  Control of motors, cameras, MicroTCA based ADCs, image processing devices
  Controls pulse arrival time in a closed loop (motor position correction depending on ADC signal)
Vacuum setups
  Control of e.g. differential pumping sections
  Typically includes several valves, pumps, and PLC-interlocks for safety
  Pressure monitoring and history trend line plotting
Courtesy of L. Wissmann

## Slide 15: Karabo in use – DAQ and data management
Large Pixel Detector (LPD) prototype testing
  Detector control (Python based)
  Data acquisition and storage (HDF5) (C++)
  Online calibration processing, analysis and correction (Python and CUDA based)
  Interaction with calibration database (Oracle)
  Full integrated run control expected in summer
LPD quadrant prototype
Visualization of a LPD quadrant in Karabo
Courtesy of S. Hauf
Server setup necessary to harvest the data

## Slide 16: Karabo in use – Data Analysis
Serial femtosecond crystallography
  Aim is to build an SFX data processing pipeline to match the high repetition rate offered at the European XFEL
  5000 images/sec
  @ 2.3 sec per image
  30% hit rate
  3500 cores needed
Linear speed up with number of cores!
Courtesy of C. Yoon

## Slide 17: Conclusions and Acknowledgements
Karabo is unique in seamlessly combining instrument control, experiment configuration, streamed data analysis and visualization
Karabo proves capable to run complex installations even today
Currently the focus is on supporting our in-house users and external collaborators -> access is on request
Its is designed for being extended easily and will be ready to execute your algorithms during the experiments
Public release of the core system under the GNU GPL license will follow in 2015
K. Weger
M. Teichmann
S. Esenov
A. Parenti
A. Beckmann
G. Giambartolomei
A. Silenzi
J. Szuba
M. Kumar
L. Maia
D. Boukhelef
S. Hauf
C. Yoon
A. Münnich
L. Wissmann
P. Geßler
K. Wrona
C. Youngman
… and many more
Stay tuned…

## Slide 18
Thank you for your kind attention.
Contact details: burkhard.heisen@xfel.eu